## Slide 1
Anjuman College of Engineering and Technology
Civil Engineering Department
Unit-1
Highway Development And Planning
TRANSPORTATION ENGINEERING-I

## Slide 2: Transportation engineering
Transportation engineering
application of technology and
is the
scientific
principles to the planning, functional design, operation and management of facilities for any mode of transportation in order to provide for the safe, efficient, rapid, comfortable, convenient, economical, and environmentally compatible movement of people and goods from one place to other.

## Slide 3: MODES OF TRANSPORTATION
Basic mode of transportation are
Land
  Roadway
  Railway
Water
Air

## Slide 4: MODES OF TRANSPORTATION
Highways
Car, Bus, Truck, non- motorized ..etc
Railways
Trains.
Airways
Aircraft and Helicopters
Waterways
Ships, boats…

## Slide 5: Airways
Fastest among all other modes
More comfortable
Time saving
Uneconomical
Waterways
slowest among all other modes
This can be possible between ports on the sea
routes or along the river
economical

## Slide 6: Railways
The transportation along the railways track could be advantageous by railways between the stations both for the passengers and goods, particularly for long distance.
It depends upon the road transport
Safety

## Slide 7: Highways
It gives the maximum service to one and all
It gives maximum flexibility for travel with reference to route, direction, time and speed of travel
It provide door to door service
It requires small investment for the government
Motor vehicles are cheaper than other carriers like rail locomotive and wagons
It saves the time for short distance
High degree of accident due to flexibility of movement

## Slide 8: Scope of highway engineering
planning and location
Highway design, geometric and structure
Traffic performance and its control
Materials, construction and maintenance
Economic, finance and administration

## Slide 9: Characteristics of road transport
Roads are used by various types of road vehicles, like passenger cars, buses, trucks, pedal cycle and animal drawn vehicle.
It requires a relatively small investment for the
government.
It offers a complete freedom to road users to transfer the vehicle from one lane to another and from one road to another according to need and convenience.
Speed and movement is directly related to the
accident.

## Slide 10: HISTORICAL DEVELOPMENT OF ROAD CONSTRUCTION
Oldest mode
  Foot paths- animal ways, cart path……..
As civilization evolved the need for transportation increased
ROMAN ROAD
They were built straight regardless of gradient
They were built after the soft soil was removed and
a hard stratum was reached.
Thickness varies from 0.75 m to 1.2m

## Slide 11: Roman Road Construction Basic cross section

## Slide 12
Modern Highway
Roman Roads

## Slide 13: Indian Roads
India has a large road network of over 3.314 million kilometers of roadways making it 3rd largest road network in the world.
National Highways - 70,548 Km
State Highways - 1,31,899 Km
Major District Roads - 4,67,763 Km
Rural Roads - 26,50,000 Km

## Slide 14: Highway Development in India
Jayakar Committee (1927)
Central Road Fund (1929)
Indian Roads Congress (IRC), 1934
Central Road Research Institute (CRRI), 1950
Motor vehicle act (1936)
National Highway Authority of India (NHAI),1995
First twenty year road plan ( 1943-61 )
Second twenty year road plan ( 1961-81 )
Third twenty year road plan ( 1981-2001 )

## Slide 15: Jayakar Committee,1927
After the first World War, motor vehicle using the roads increases, this demanded a better road network.
In 1927,Indian road development committee was appointed
by the government with M.R. Jaykar as chairman.
Road development in the country should be made as a national interest since local govt. do not have financial and technical capacity for road development.
An extra tax should be on petrol from road users to
create the road development fund.
To create a national level institution to carry research , development works and consultation.

## Slide 16: Central road fund
It was formed on 1st march 1929
The consumers of petrol were charged an extra 2.64 paisa per litre of petrol to built up this road development fund.
From this 20% of annual reveneu is to be retain as a central reveneu for research and experimental work expenses. etc
Balance 80% is allowed by central govt. to various states based on actual petrol consumption

## Slide 17: Central Road Fund , 1929
Distribution of 100% on petrol as follows:
57.5% for NH
30% for SH
12.5% for safety works on rail-Road crossing.
50% on diesel for Rural Road development

## Slide 18: Indian Roads Congress, 1934
Central semi official body known as IRC was formed in 1934.
To provide ideas related to construction and maintenance of highways.
It is a active body controlling the specification, standardization and recommendations on materials, design of roads and bridges.
It publishes journals, research publications and standard specifications guide lines.

## Slide 19: Motor vehicle act
It was formed in 1939
To regulate the road traffic in the form of
traffic laws, ordinances and regulations.
Three phases primarily covered are control of driver, vehicle ownership and vehicle operation
It was revised on 1988

## Slide 20: Central road research institute(1950)
engaged in carrying out
projects.
design, construction and
research and development
maintenance of roads and
runways, traffic and transportation planning of mega and medium cities, management of roads in different slopes,
Utilization of industrial waste in road construction.
Landslide control.
Ground improvements, environmental pollution.
Road traffic safety.

## Slide 21: Classification of Highways
Based on the Traffic
Heavy
Medium
Light
Based on location and function ( Nagpur road plan )
National highway (NH)
State highway (SH)
Major district road (MDR)
Other district road (ODR)
Village road (VR)

## Slide 22: Based on modified system of Highways classification
Primary
  Expressways
  National Highways
Secondary
  State Highway
  Major District Road
Tertiary
  Other District Road
  Village Road

## Slide 23: Expressways
Heavy traffic at high speed (120km/hrs)
Connects major points of traffic generation
No slow moving traffic allowed
No loading,
The Mumbai-Pune Expressway as seen from Khandala

## Slide 24: National Highways
NH are the main highways running through the length and breadth of India, connecting major parts, capital of large states and large industrial and tourist centers.
The national highways have a total length of 70,548 kms. Indian highways cover 2% of the total road network of India and carry 40% of the total traffic.
The highway connecting Delhi-Ambala-Amritsar is denoted as NH-1, whereas a bifurcation of this highway beyond Jalandar to Srinagar is denoted NH-1-A
The longest highway in India is NH-7 which stretches from Varansi in Uttar Pradesh to Kanyakumari.

## Slide 25: National Highways cont…
ms) connecting Delhi-
)
The shortest highway is NH47A which stretches from Ernakulam to Kochi and covers total length of 4 Kms.
Golden Quadrilateral – (5,846 K
Kolkata-Chennai-Mumbai
  NH-2 Delhi- Kol (1453 km)
 NH 4,7 Che-Mum (1290km)
 NH5&6 Kol- Che (1684 Km)
  NH 8 Del- Mum (1419 km)

## Slide 26: State Highways
They are the roads of a state, connecting up with the national highways of adjacent states, district head quarters and important cities within the state.
Total length of all SH in the country is
1,37,119 Kms.
Speed 80 kmph

## Slide 27: Major District Roads
Important roads with in a district serving areas of production and markets , connecting those with each other or with the major highways.
India has a total of 4,70,000 kms of MDR.
Speed 60-80kmph

## Slide 28: Other district roads
serving rural areas of production
centers
and providing
or other
They are roads connecting villages or group of villages with each other or to the nearest road of a higher category like ODR or MDR.
ODR+VR out of the total 33,15,231 kms of all type of roads.
Speed-40-50 kmph
them with outlet to market important roads like MDR or SH.
Speed 50-60kmph
Village roads

## Slide 29: First 20-years road plan(1943-63)
The conference of chief engineer held at Nagpur in 1943 finalized the first 20-years road development plan for India called Nagpur road plan
Road network was classified into five categories.
The responsibility of construction maintenance of NH was assign to central govt.
The target road length was 5,32,700 km at the end of 1961.

## Slide 30: First 20-years road plan cont…
The formulae were based on star and grid pattern of road network.
An allowance of 15% is provided for agricultural and industrial development during the next 20-years
The length of railway track in the area was also consider in deciding the length of first category road. The length or railway track is directly subtracted from the estimated road.

## Slide 31: Second 20-years road plan(1961-81)
It was initiated by the IRC and was finalised in 1959 at the meeting of chief engineers.
It is known as the Bombay road plan.
The target road length was almost double that of Nagpur road plan i.e. 10,57,330 km.

## Slide 32: Second 20-years road plan cont…
the maximum distance from any place in a semi develop area would be 4.8 Km from any road
Expressways have also been considered in this plan and 1600 km of length has been included in the proposed target NH
Length of railway track is considered
independent of road system
5% are to be provided for future development.

## Slide 33: Third twenty years road plan (1981-2001)
The future road development should be based on the revised classification of roads system i.e. primary, secondary and tertiary
Develop the rural economy and small towns with all essential features.
Population over 500 should be connected by all roads.

## Slide 34: Third twenty years road plan
cont…
Expressway should be constructed along major traffic consideration.
All towns and villages with population over 1500 should be connected by MDR and villages with population 1000-1500 by ODR.
Road should be built in less industrialized areas to attract the growth of industries
The existing roads should be improved by rectifying the defects in the road geometry, widening, riding quality and strengthening the existing pavement to save vehicle operation cost and thus to conserve energy

## Slide 35
Highway alignment and surveys

## Slide 36: Highway alignment
The position or lay out of centre line of the highway on the ground is called the alignment.
It includes straight path, horizontal deviation and
curves.
Due to improper alignment , the disadvantages are,
  Increase in construction
  Increase in maintenance cost
  Increase in vehicle operation cost
  Increase in accident cost
Once the road is aligned and constructed, it is not easy to change the alignment due to increase in cost of adjoining land and construction of costly structure.

## Slide 40: Requrements of highway alignment
Short
Easy
Safe
Economical
Short- desirable to have a short alignment between two
terminal stations.
Easy- easy to construct and maintain the road with minimum problem also easy for operation of vehicle.
Safe- safe enough for construction and maintenance from the view point of stability of natural hill slope, embankment and cut slope also safe for traffic operation.
Economical- total cost including initial cost, maintenance cost and vehicle operation cost should be minimum.

## Slide 41: Factors controlling alignment
Obligatory points
Traffic
Geometric design
Economics
Other considerations Additional care in hill roads
Stability
Drainage
Geometric standards of hill roads
Resisting length

## Slide 42: Factors controlling alignment cont...
Obligatory points
Obligatory points through which alignment is to pass
Examples:-bridge site, intermediate town , Mountain pass etc…
Obligatory points through which alignment should not
pass.
Examples:-religious places, costly structure, unsuitable land etc…
Traffic
origin and destination survey should be carried out in the area and the desire lines be drawn showing the trend of traffic flow.
New road to be aligned should keep in view the desired lines, traffic flow patterns and future trends.

## Slide 43: Geometric design
Design factors such as gradient ,radius of curve and sight distance also govern the final alignment of the highway.
Gradient should be flat and less than the ruling gradient or design gradient.
Avoid sudden changes in sight distance, especially near crossings
Avoid sharp horizontal curves
Avoid road intersections near bend
Economy
Alignment finalised based on total cost including initial cost, maintenance cost and vehicle operation cost.
Other consideration
Drainage consideration, political consideration
Surface water level, high flood level
Environmental consideration

## Slide 44: Topographical control points
The alignment, where possible should avoid passing through
  Marshy and low lying land with poor drainage
  Flood prone areas
  Unstable hilly features
Materials and constructional features
  Deep cutting should be avoided
  Earth work is to be balanced; quantities for filling and excavation
  Alignment should preferably be through better soil area to minimize pavement thickness
  Location may be near sources of embankment and pavement materials

## Slide 45: stability
A common problem in hilly roads is land sliding
The cutting and filling of the earth to construct the roads on hilly sides causes steepening of existing slope and affect its stability.
Drainage
Avoid the cross drainage structure
The number of cross drainage structure should be minimum.
Geometric standard of hilly road
Gradient, curve and speed
Sight distance, radius of curve
Resisting length
The total work to be done to move the loads along the route taking horizontal length, the actual difference in level between two stations and the sum of the ineffective rise and fall in excess of floating gradient. Should kept as low as possible.

## Slide 46: Engineering Surveys for Highway locations
Before a highway alignment is finalised in highway project, the engineering survey are to be carried out. The various stages of engineering surveys are
Map study (Provisional alignment Identification)
Reconnaissance survey
Preliminary survey
Final location and detailed surveys

## Slide 47: MAP STUDY
From the map alternative routes can be suggested in the office, if the topographic map of that area is available.
The probable alignment can be located on the map from the fallowing details available on the map.
Avoiding valleys, ponds or lake
Avoiding bend of river
If road has to cross a row of hills, possibility of crossing through mountain pass.
Map study gives a rough guidance of the routes to
be further surveyed in the field

## Slide 48: RECONNAISSANCE SURVEY
To confirm features indicated on map.
To examine the general character of the area in field for deciding the most feasible routes for detailed studies.
A survey party may inspect along the proposed alternative routes of the map in the field with very simple instrument like abney level, tangent clinometer, barometer etc…. To collect additional details.
Details to be collected from alternative routes during this
survey are,
  Valleys, ponds, lakes, marshy land, hill, permanent
structure and other obstruction.
  Value of gradient, length of gradient and radius of curve.

## Slide 49: RECONNAISSANCE SURVEY cont..
Number and type of cross drainage structures.
  High Flood Level (HFL)
  Soil Characteristics.
  Geological features.
  source of construction materials- stone quarries, water
sources.
Prepare a report on merits and demerits of different alternative routs.
As a result a few alternate alignments may be chosen for further study based on practical considerations observed at the site.

## Slide 50: Preliminary survey
Objective of preliminary survey are:
To survey the various alternative alignments proposed after the reconnaissance and to collect all the necessary physical information and detail of topography, drainage and soil.
To compare the different proposals in view of the requirements of the good alignment.
To estimate quantity of earthwork materials and other construction aspect and to workout the cost of the alternate proposals.
Methods of preliminary survey:
a) Conventional approach-survey party carries out surveys using the required field equipment, taking measurement, collecting topographical and other data and carrying out soil survey.

## Slide 51: Preliminary survey cont…
Longitudinal and cross sectional profile.
: 100 – 200m
: 50m
: 30m
Plain Terrain`
Rolling Terrain
Hilly Terrain
Other studies
Drainage, Hydrological survey, soil survey, Traffic and
Material survey.
b) Modern rapid approach-
By Aerial survey taking the required aerial photographs for obtaining the necessary topographic and other maps including details of soil and geology.
Finalise the best alignment from all considerations by comparative analysis of alternative routes.

## Slide 52: Final location and detailed survey
The alignment finalised at the design office after the preliminary survey is to be first located on the field by establishing the centre line.
Location survey:
Transferring the alignment on to ground.
This is done by transit theodolite.
Major and minor control points are established on the ground and centre pegs are driven, checking the geometric design requirements.
Centre line stacks are driven at suitable intervals, say 50m interval in plane and rolling terrains and 20m in hilly terrain.

## Slide 53: Final location and detailed survey
cont..
Detailed survey:
Temporary bench marks are fixed at intervals of about 250m and at all drainage and under pass structure.
Earthwork calculations and drainage details are to be workout from the level books.
Cross sectional levels are taken at intervals of 50-100m in Plane terrain, 50-75m in Rolling terrain, 50m in built-up area, 20m in Hill terrain.
Detail soil survey is to be carried out.
CBR value of the soils along the alignment may be determined
for design of pavement.
The data during detailed survey should be elaborate and complete for preparing detailed plans, design and estimates of project.

## Slide 54: Drawing and Report
Key map
Index map
Preliminary survey plans
Detailed plan and longitudinal section
Detailed cross section
Land acquisition plans
Drawings of cross drainage and other retaining
structures
Drawings of road intersections
Land plans showing quarries etc

## Slide 55: New highway project
Map study
Reconnaissance survey
Preliminary survey
Location of final alignment
Detailed survey
Material survey
Geometric and structural design
Earth work
Pavement construction
Construction controls

## Slide 56: Bibliography
Khanna, S. K., & Justo, C. E. G. Highway
engineering. Nem Chand & Bros.
IRC Codes.

## Slide 57: Two lane two-way road
carriageway

## Slide 58: shoulder
Footpath
Cycle track

## Slide 59
unTreated shoulder
Treated
shoulder

## Slide 60: 4-lane divided carriage way or dual carriage way
Median/
separator

## Slide 61
kerb

## Slide 62
Frontage
road

## Slide 64: Guard rails

## Slide 65
Horizontal
curve

## Slide 66: Rigid Pavement

## Slide 67: Flexible pavement
Rigid pavement

## Slide 68
Distribution of pressure

## Slide 69
FLEXIBLE PAVEMENT
RIGID PAVEMENT